Camera Calibration

Introduction
Camera maps the information in the 3D world to the information in the 2D image. Thus the camera projects 3D world points to their corresponding 2D image points This mapping can be mathematically expressed as shown in equation 5.1
{ P} rsub {c =} {C} rsub {3×4 } {P} rsub {world } Eq 5.1
where, {C} rsub {3×4 } is a camera projection matrix of size 3 by 4
{P} rsub {world } is a world point
{P} rsub {c } is an image point
Determining the camera projection matrix and its elements is termed as ‘camera calibration’. The camera projection matrix can be expressed in the form of its elements as given in equation 5.2
{C} rsub {3×4 } = left [matrix {{c} rsub {11} # {c} rsub {12} # {c} rsub {13} ## {c} rsub {21} # {c} rsub {22} # {c} rsub {23} ## {c} rsub {31} # {c} rsub {32} # {c} rsub {33}} matrix {{c} rsub {14} ## {c} rsub {24} ## {c} rsub {34}} right ] Eq.5. 2

The plane which passes through camera projection centre and parallel to focal (image) plane is termed as the principal plane. The ray orthogonal to the principal plane and originating from the camera projection centre passes through the focal plane of the camera. This point of intersection is the principal point of the camera. This point can be determined as follows-
 The camera matrix can be decomposed as,
{ C} rsub {3×4 } = left [M | {C} rsub {4} right ] Eq.5. 3
Where, M is a sub matrix with first three columns of the camera matrix and C4 is fourth column of the camera matrix. Thus { C} rsub {3×4 } is an augmented matrix.
The graphical representation for the transformation expressed in the equation is- (The Pinhole model is the most widely used model which is also demonstrated here)

(Actually the image will form on the other end of a simple pin-hole camera but it is projected on the other side for ease in handling the situation.)
The mapping of object point P(X,Y,Z) to its corresponding image point Pc is described by equations 5.4 and 5.5

P↦ {P} rsub {c} Eq.5.4

left [matrix {X ## Y ## Z} right ] ↦ left [matrix {u ## v} right ] Eq .5.5
An intelligent approach is to utilise X,Y and Z to define u and v. Thus in homogenous system u and v are-
 u= f X left ({X} over {Z} right ) and v= f X left ({Y} over {Z} right )
Hence,
left [matrix {X ## Y ## Z} right ] ↦ left [matrix {f {X} over {Z} ## f {Y} over {Z}} right ] Eq.5.6
OR

left [matrix {X ## Y ## Z ## 1} right ] → left (left [matrix {fX ## fY ## Z} right ] = left [matrix {f # 0 # 0 ## 0 # f # 0 ## 0 # 0 # 1} matrix {0 ## 0 ## 0} right ] left [matrix {X ## Y ## Z ## 1} right ] right ) Eq.5.7

The pinhole model described above assumes that the origin of the focal (or the image) plane is at its centre which also happens to be the principal point of the camera. In practice, the origin of the focal (image) plane may not be the principal point. ( Usually it is at one corner of the image plane)

Hence,
left [matrix {X ## Y ## Z ## 1} right ] ↦ left [matrix {fX+Z {t} rsub {u} ## fY+Z {t} rsub {v} ## Z} right ] = left [matrix {f # 0 # {t} rsub {u} ## 0 # f # {t} rsub {v} ## 0 # 0 # 1} matrix {0 ## 0 ## 0} right ] left [matrix {X ## Y ## Z ## 1} right ] Eq.5.8
where, (tu,tv) are the coordinates of the principal point of the camera with respect to the origin of the image plane. ( Multiplied by Z in the homogenous system).

Normally, the pixels in the image are square shaped. If the pixels of the image are not square shaped, the pixel resolution in the image in the direction of u axis will be different than pixel resolution in the direction of v axis. Let and {m} rsub {v} represent camera pixel resolution along u and v axes. Hence,

Here we can write {{f} rsub {x} instead of m} rsub {u} f and

The more general form of the above equation is by considering skew parameter ‘s’

left [matrix {X ## Y ## Z ## 1} right ] ↦ left [matrix {fX+Z {t} rsub {u} ## fY+Z {t} rsub {v} ## Z} right ] = left [ matrix {{f} rsub {x} # s # {t} rsub {u} ## 0 # {f} rsub {y} # {t} rsub {v} ## 0 # 0 # 1} matrix {0 ## 0 ## 0} right ] left [matrix {X ## Y ## Z ## 1} right ] Eq.5.10
The skew parameter is zero in most of the normal cameras. Actually Open-CV does not consider skew. Thus the equation becomes-
left [matrix {u ## v} right ] = left [ matrix {{f} rsub {x} # 0 # {t} rsub {u} ## 0 # {f} rsub {y} # {t} rsub {v} ## 0 # 0 # 1} right ] left [matrix {X ## Y ## Z} right ] Eq.5.11
Img = {K} rsub {3×3} X P Eq.5.12

where, {K} rsub {3×3} is called as intrinsic parameter matrix of the camera.

Here, and {f} rsub {v} represents the camera focal lengths (in pixels), and {m} rsub {v} represent camera pixel resolution along u and v axes of the camera, whereas {t} rsub {u} and {t} rsub {v} represent the principal point coordinates in pixel units. All these elements of matrix K are called as intrinsic parameters of the camera. Thus the intrinsic parameters of camera need to be determined to relate the camera coordinate system and image coordinate system. The mapping equation expressed assumes that the camera centre is at the origin of the real-world coordinate system which may not be the case in practical situations.
Hence the rotation and translation matrices are used. The translation vector ‘t’ and the rotation matrix ‘R’ are the extrinsic parameters of the camera.
Thus final equation becomes-
Img=K* left [R:t right ] *P Eq.5.12
Where R:t is called the extrinsic matrix.
Thus the final equation becomes-
{ P} rsub {c} = C . P Eq .5.13
Where the camera matrix {C} rsub {3 × 4} is,
{C} rsub {3 × 4} = left [{K} rsub {3×3} ][ {R} rsub {3×3} : {t} rsub {3×1} right ] Eq.5.14

Thus to fully calibrate the camera, all the elements of camera matrix, {C} rsub {3 × 4} need to be determined.
(Need of homogenous set of equation- To represent infinity)

________________________________________________________________________________________________________________________________

Result-
For Program implementation using webcam
corners:[[[[691. 343.]
   [743. 343.]
   [739. 401.]
   [687. 399.]]]

 [[[896. 423.]
   [961. 426.]
   [960. 492.]
   [893. 487.]]]

 [[[821. 420.]
   [882. 423.]
   [879. 487.]
   [818. 481.]]]

 [[[751. 417.]
   [807. 419.]
   [804. 481.]
   [748. 476.]]]

 [[[686. 414.]
   [738. 416.]
   [735. 475.]
   [683. 471.]]]

 [[[899. 344.]
   [964. 344.]
   [961. 410.]
   [896. 406.]]]

 [[[825. 343.]
   [885. 344.]
   [882. 406.]
   [822. 404.]]]

 [[[755. 343.]
   [810. 343.]
   [807. 404.]
   [752. 402.]]]

 [[[695. 275.]
   [746. 272.]
   [744. 328.]
   [692. 329.]]]

 [[[759. 272.]
   [813. 269.]
   [811. 329.]
   [756. 329.]]]

 [[[829. 269.]
   [888. 268.]
   [884. 329.]
   [825. 328.]]]

 [[[902. 267.]
   [967. 265.]
   [964. 329.]
   [899. 328.]]]

 [[[677. 294.]
   [736. 295.]
   [731. 356.]
   [672. 354.]]]

 [[[905. 377.]
   [976. 380.]
   [974. 448.]
   [903. 445.]]]

 [[[823. 375.]
   [889. 376.]
   [887. 443.]
   [820. 440.]]]

 [[[745. 372.]
   [808. 375.]
   [805. 439.]
   [741. 435.]]]

 [[[671. 370.]
   [731. 371.]
   [727. 435.]
   [667. 432.]]]

 [[[909. 294.]
   [978. 295.]
   [976. 362.]
   [905. 359.]]]

 [[[827. 294.]
   [892. 294.]
   [889. 360.]
   [824. 358.]]]

 [[[750. 294.]
   [811. 294.]
   [808. 358.]
   [746. 356.]]]

 [[[683. 222.]
   [740. 220.]
   [735. 280.]
   [678. 280.]]]

 [[[754. 220.]
   [815. 217.]
   [812. 279.]
   [750. 279.]]]

 [[[830. 218.]
   [895. 216.]
   [892. 279.]
   [827. 279.]]]

 [[[910. 216.]
   [980. 215.]
   [978. 279.]
   [908. 279.]]]

 [[[691. 343.]
   [743. 343.]
   [739. 401.]
   [687. 399.]]]

 [[[896. 423.]
   [961. 426.]
   [960. 492.]
   [893. 487.]]]

 [[[821. 420.]
   [882. 423.]
   [879. 487.]
   [818. 481.]]]

 [[[751. 417.]
   [807. 419.]
   [804. 481.]
   [748. 476.]]]

 [[[686. 414.]
   [738. 416.]
   [735. 475.]
   [683. 471.]]]

 [[[899. 344.]
   [964. 344.]
   [961. 410.]
   [896. 406.]]]

 [[[825. 343.]
   [885. 344.]
   [882. 406.]
   [822. 404.]]]

 [[[755. 343.]
   [810. 343.]
   [807. 404.]
   [752. 402.]]]

 [[[695. 275.]
   [746. 272.]
   [744. 328.]
   [692. 329.]]]

 [[[759. 272.]
   [813. 269.]
   [811. 329.]
   [756. 329.]]]

 [[[829. 269.]
   [888. 268.]
   [884. 329.]
   [825. 328.]]]

 [[[902. 267.]
   [967. 265.]
   [964. 329.]
   [899. 328.]]]

 [[[691. 343.]
   [743. 343.]
   [739. 401.]
   [687. 399.]]]

 [[[896. 423.]
   [961. 426.]
   [960. 492.]
   [893. 487.]]]

 [[[821. 420.]
   [882. 423.]
   [879. 487.]
   [818. 481.]]]

 [[[751. 417.]
   [807. 419.]
   [804. 481.]
   [748. 476.]]]

 [[[686. 414.]
   [738. 416.]
   [735. 475.]
   [683. 471.]]]

 [[[899. 344.]
   [964. 344.]
   [961. 410.]
   [896. 406.]]]

 [[[825. 343.]
   [885. 344.]
   [882. 406.]
   [822. 404.]]]

 [[[755. 343.]
   [810. 343.]
   [807. 404.]
   [752. 402.]]]

 [[[695. 275.]
   [746. 272.]
   [744. 328.]
   [692. 329.]]]

 [[[759. 272.]
   [813. 269.]
   [811. 329.]
   [756. 329.]]]

 [[[829. 269.]
   [888. 268.]
   [884. 329.]
   [825. 328.]]]

 [[[902. 267.]
   [967. 265.]
   [964. 329.]
   [899. 328.]]]

 [[[616. 368.]
   [674. 365.]
   [678. 423.]
   [620. 425.]]]

 [[[613. 298.]
   [669. 295.]
   [673. 350.]
   [616. 354.]]]

 [[[683. 295.]
   [738. 292.]
   [744. 346.]
   [687. 350.]]]

 [[[541. 237.]
   [596. 233.]
   [599. 286.]
   [543. 289.]]]

 [[[475. 376.]
   [532. 372.]
   [534. 429.]
   [476. 433.]]]

 [[[545. 372.]
   [603. 369.]
   [605. 426.]
   [547. 429.]]]

 [[[687. 365.]
   [744. 361.]
   [749. 418.]
   [691. 421.]]]

 [[[474. 306.]
   [530. 303.]
   [531. 358.]
   [475. 362.]]]

 [[[543. 302.]
   [599. 299.]
   [602. 354.]
   [545. 358.]]]

 [[[473. 241.]
   [528. 237.]
   [530. 289.]
   [474. 293.]]]

 [[[609. 234.]
   [665. 230.]
   [669. 282.]
   [613. 285.]]]

 [[[678. 230.]
   [733. 227.]
   [738. 279.]
   [682. 282.]]]

 [[[691. 343.]
   [743. 343.]
   [739. 401.]
   [687. 399.]]]

 [[[896. 423.]
   [961. 426.]
   [960. 492.]
   [893. 487.]]]

 [[[821. 420.]
   [882. 423.]
   [879. 487.]
   [818. 481.]]]

 [[[751. 417.]
   [807. 419.]
   [804. 481.]
   [748. 476.]]]

 [[[686. 414.]
   [738. 416.]
   [735. 475.]
   [683. 471.]]]

 [[[899. 344.]
   [964. 344.]
   [961. 410.]
   [896. 406.]]]

 [[[825. 343.]
   [885. 344.]
   [882. 406.]
   [822. 404.]]]

 [[[755. 343.]
   [810. 343.]
   [807. 404.]
   [752. 402.]]]

 [[[695. 275.]
   [746. 272.]
   [744. 328.]
   [692. 329.]]]

 [[[759. 272.]
   [813. 269.]
   [811. 329.]
   [756. 329.]]]

 [[[829. 269.]
   [888. 268.]
   [884. 329.]
   [825. 328.]]]

 [[[902. 267.]
   [967. 265.]
   [964. 329.]
   [899. 328.]]]

 [[[459. 383.]
   [519. 383.]
   [523. 441.]
   [462. 443.]]]

 [[[532. 382.]
   [588. 381.]
   [593. 439.]
   [536. 441.]]]

 [[[602. 381.]
   [656. 380.]
   [661. 437.]
   [607. 439.]]]

 [[[668. 380.]
   [719. 380.]
   [725. 434.]
   [674. 436.]]]

 [[[661. 313.]
   [711. 314.]
   [717. 366.]
   [667. 367.]]]

 [[[596. 311.]
   [648. 312.]
   [654. 367.]
   [601. 367.]]]

 [[[527. 311.]
   [583. 311.]
   [587. 367.]
   [531. 367.]]]

 [[[653. 250.]
   [701. 252.]
   [709. 301.]
   [659. 300.]]]

 [[[455. 311.]
   [514. 311.]
   [517. 367.]
   [458. 368.]]]

 [[[590. 246.]
   [641. 249.]
   [647. 300.]
   [595. 299.]]]

 [[[522. 244.]
   [577. 246.]
   [582. 298.]
   [526. 297.]]]

 [[[452. 242.]
   [509. 243.]
   [513. 297.]
   [455. 297.]]]

 [[[609. 404.]
   [668. 407.]
   [669. 469.]
   [609. 468.]]]

 [[[680. 333.]
   [734. 337.]
   [736. 396.]
   [681. 392.]]]

 [[[607. 328.]
   [666. 332.]
   [667. 392.]
   [608. 388.]]]

 [[[677. 263.]
   [731. 269.]
   [733. 324.]
   [679. 319.]]]

 [[[815. 414.]
   [865. 417.]
   [867. 474.]
   [818. 472.]]]

 [[[751. 411.]
   [803. 414.]
   [806. 472.]
   [752. 470.]]]

 [[[682. 408.]
   [737. 410.]
   [739. 471.]
   [683. 470.]]]

 [[[811. 344.]
   [859. 348.]
   [864. 402.]
   [814. 399.]]]

 [[[747. 338.]
   [799. 342.]
   [802. 399.]
   [750. 396.]]]

 [[[806. 277.]
   [853. 283.]
   [858. 335.]
   [810. 330.]]]

 [[[744. 270.]
   [794. 276.]
   [798. 329.]
   [747. 325.]]]

 [[[607. 256.]
   [664. 262.]
   [666. 318.]
   [607. 313.]]]

 [[[691. 343.]
   [743. 343.]
   [739. 401.]
   [687. 399.]]]

 [[[896. 423.]
   [961. 426.]
   [960. 492.]
   [893. 487.]]]

 [[[821. 420.]
   [882. 423.]
   [879. 487.]
   [818. 481.]]]

 [[[751. 417.]
   [807. 419.]
   [804. 481.]
   [748. 476.]]]

 [[[686. 414.]
   [738. 416.]
   [735. 475.]
   [683. 471.]]]

 [[[899. 344.]
   [964. 344.]
   [961. 410.]
   [896. 406.]]]

 [[[825. 343.]
   [885. 344.]
   [882. 406.]
   [822. 404.]]]

 [[[755. 343.]
   [810. 343.]
   [807. 404.]
   [752. 402.]]]

 [[[695. 275.]
   [746. 272.]
   [744. 328.]
   [692. 329.]]]

 [[[759. 272.]
   [813. 269.]
   [811. 329.]
   [756. 329.]]]

 [[[829. 269.]
   [888. 268.]
   [884. 329.]
   [825. 328.]]]

 [[[902. 267.]
   [967. 265.]
   [964. 329.]
   [899. 328.]]]]
ids_list:[[ 5]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 1]
 [ 2]
 [ 3]
 [ 4]
 [ 5]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 1]
 [ 2]
 [ 3]
 [ 4]
 [ 5]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 1]
 [ 2]
 [ 3]
 [ 4]
 [ 5]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 1]
 [ 2]
 [ 3]
 [ 4]
 [11]
 [ 7]
 [ 8]
 [ 2]
 [ 9]
 [10]
 [12]
 [ 5]
 [ 6]
 [ 1]
 [ 3]
 [ 4]
 [ 5]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 1]
 [ 2]
 [ 3]
 [ 4]
 [ 9]
 [10]
 [11]
 [12]
 [ 8]
 [ 7]
 [ 6]
 [ 4]
 [ 5]
 [ 3]
 [ 2]
 [ 1]
 [ 9]
 [ 6]
 [ 5]
 [ 2]
 [12]
 [11]
 [10]
 [ 8]
 [ 7]
 [ 4]
 [ 3]
 [ 1]
 [ 5]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 1]
 [ 2]
 [ 3]
 [ 4]]
Intrinsic Camera Matrix
[[ 1.00300964e+03 0.00000000e+00 -4.57525034e+02]
 [ 0.00000000e+00 4.42652128e+02 9.22497481e+02]
 [ 0.00000000e+00 0.00000000e+00 1.00000000e+00]]
Extrinsic Camera Parameters
R_vecs
[array([[-2.19737745],
       [-0.99491132],
       [ 1.60990966]]), array([[-2.16976798],
       [-0.91647861],
       [ 1.59443824]]), array([[-2.19737745],
       [-0.99491132],
       [ 1.60990966]]), array([[-2.19737745],
       [-0.99491132],
       [ 1.60990966]]), array([[-2.82536566],
       [ 0.47579947],
       [-0.87208236]]), array([[-2.19737745],
       [-0.99491132],
       [ 1.60990966]]), array([[ 3.03827445],
       [-0.50706223],
       [ 0.97975207]]), array([[ 3.14678772],
       [-0.39490319],
       [ 0.88266793]]), array([[-2.19737745],
       [-0.99491132],
       [ 1.60990966]])]
T_vecs
[array([[ 0.1929214 ],
       [-0.15460879],
       [ 0.23531072]]), array([[ 0.20146714],
       [-0.17480563],
       [ 0.2443662 ]]), array([[ 0.1929214 ],
       [-0.15460879],
       [ 0.23531072]]), array([[ 0.1929214 ],
       [-0.15460879],
       [ 0.23531072]]), array([[ 0.20249637],
       [-0.20151747],
       [ 0.27564145]]), array([[ 0.1929214 ],
       [-0.15460879],
       [ 0.23531072]]), array([[ 0.19598563],
       [-0.19311598],
       [ 0.26960371]]), array([[ 0.2018271 ],
       [-0.15522637],
       [ 0.23719006]]), array([[ 0.1929214 ],
       [-0.15460879],
       [ 0.23531072]])]
Size of the image (using shape function) =720,1280 pixels
________________________________________________________________________________________________________________________________

Result –
For program implementation using mobile phone camera

corners:[[[[442. 484.]
   [485. 486.]
   [482. 529.]
   [440. 526.]]]

 [[[391. 482.]
   [433. 484.]
   [431. 527.]
   [389. 525.]]]

 [[[338. 480.]
   [381. 483.]
   [379. 525.]
   [337. 523.]]]

 ...

 [[[341. 354.]
   [385. 357.]
   [382. 402.]
   [339. 399.]]]

 [[[287. 350.]
   [331. 354.]
   [329. 398.]
   [285. 395.]]]

 [[[233. 346.]
   [277. 350.]
   [275. 394.]
   [231. 391.]]]]
ids_list:[[12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [ 6]
 [ 5]
 [ 4]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 2]
 [ 1]
 [ 3]
 [12]
 [11]
 [10]
 [ 9]
 [ 7]
 [ 8]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 3]
 [ 2]
 [ 1]
 [ 4]
 [12]
 [11]
 [10]
 [ 9]
 [ 7]
 [ 6]
 [ 8]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [ 6]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 5]
 [ 3]
 [ 6]
 [ 4]
 [ 2]
 [ 1]
 [12]
 [11]
 [10]
 [ 9]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]
 [ 8]
 [12]
 [11]
 [10]
 [ 9]
 [ 8]
 [ 7]
 [ 6]
 [ 5]
 [ 4]
 [ 3]
 [ 2]
 [ 1]]
Intrinsic Camera Matrix
[[257.34009637 0. 602.88111388]
 [ 0. 243.54297745 189.3356733 ]
 [ 0. 0. 1. ]]
Extrinsic Camera Parameters
R_vecs
[array([[0.89147451],
       [0.06381024],
       [1.49432147]]), array([[0.90148458],
       [0.09757184],
       [1.15986976]]), array([[1.58858787],
       [0.39499866],
       [1.04526763]]), array([[ 0.79235602],
       [-0.0465023 ],
       [ 1.89863387]]), array([[ 2.9853125 ],
       [-0.27744289],
       [-0.47025134]]), array([[1.17680889],
       [0.16157322],
       [1.42015508]]), array([[1.52674243],
       [0.36018961],
       [1.29120238]]), array([[1.04894227],
       [0.08757869],
       [1.61986746]]), array([[1.04894227],
       [0.08757869],
       [1.61986746]]), array([[1.67364081],
       [0.39833064],
       [1.37585792]]), array([[1.77163662],
       [0.4086198 ],
       [1.39811629]]), array([[1.62639605],
       [0.40628807],
       [1.13360151]]), array([[1.61738773],
       [0.39990955],
       [1.2227614 ]]), array([[1.16674985],
       [0.1717056 ],
       [1.41222883]]), array([[1.39934564],
       [0.24954635],
       [1.47703297]]), array([[1.05516636],
       [0.095713 ],
       [1.57938887]]), array([[-2.57615219],
       [-1.07646831],
       [-0.45056633]]), array([[1.09057704],
       [0.13445199],
       [1.35421778]]), array([[1.28183151],
       [0.20721364],
       [1.42885188]]), array([[1.42638501],
       [0.28049528],
       [1.42284362]]), array([[1.01032564],
       [0.1190258 ],
       [1.32679621]]), array([[1.39679237],
       [0.30555829],
       [1.1764111 ]]), array([[1.05408869],
       [0.10268914],
       [1.52923848]]), array([[1.54291601],
       [0.38587684],
       [1.28999661]]), array([[0.81249503],
       [0.02202119],
       [1.7443075 ]])]
T_vecs
[array([[-0.07172931],
       [ 0.08846801],
       [ 0.06245533]]), array([[-0.06095047],
       [ 0.13016888],
       [ 0.079389 ]]), array([[-0.00733045],
       [ 0.08392621],
       [ 0.05416222]]), array([[-0.03897786],
       [ 0.02458459],
       [ 0.02208502]]), array([[-0.08878069],
       [ 0.10945081],
       [ 0.08730928]]), array([[-0.05309204],
       [ 0.07019583],
       [ 0.04992457]]), array([[-0.02825442],
       [ 0.06756412],
       [ 0.04624193]]), array([[-0.05227693],
       [ 0.04523824],
       [ 0.03703573]]), array([[-0.05227693],
       [ 0.04523824],
       [ 0.03703573]]), array([[-0.02561965],
       [ 0.04750632],
       [ 0.03542198]]), array([[-0.02413637],
       [ 0.04555146],
       [ 0.03719789]]), array([[-0.01198064],
       [ 0.06768113],
       [ 0.04510582]]), array([[-0.01766266],
       [ 0.06310427],
       [ 0.04292311]]), array([[-0.06035143],
       [ 0.08129877],
       [ 0.0588886 ]]), array([[-0.04307903],
       [ 0.05234001],
       [ 0.03915726]]), array([[-0.05460975],
       [ 0.05183633],
       [ 0.04098759]]), array([[-0.0252532 ],
       [ 0.04068522],
       [ 0.03431308]]), array([[-0.05845196],
       [ 0.09297847],
       [ 0.06313379]]), array([[-0.04931874],
       [ 0.06325316],
       [ 0.04603052]]), array([[-0.04283303],
       [ 0.05982784],
       [ 0.04383079]]), array([[-0.06402543],
       [ 0.10252613],
       [ 0.06871603]]), array([[-0.03401152],
       [ 0.10187975],
       [ 0.06658995]]), array([[-0.05315655],
       [ 0.05620141],
       [ 0.04187131]]), array([[-0.02893322],
       [ 0.06929272],
       [ 0.04789309]]), array([[-0.07739113],
       [ 0.06766236],
       [ 0.0546507 ]])]

Size of the image (using shape function) =1160, 868 pixels